## Slide 1
Router
Network: HIT-FRITZBOX-7490
Web Browser
Microcontroller
(ESP32)
Get
Ip Address
Get
Ip Address
Data
Action

## Slide 2
START ESP32
User insert IP Address?
A
B
C
D
E
IP Address displayed?
No
No
Yes
Yes
No
Yes
IP Address connected?
Connect Server and Client
Connect to internet

## Slide 3
A
Light Intensity checked?
<35 Lux
35 to 55 Lux
>100 Lux
Display Status on Browser:
“Dark
Less than 35 Lux”
Display Status on Browser:
“Dim
35 Lux to 55 Lux”
Display Status on Browser:
“Very Bright
More than 100 Lux”
No
Display Status on Browser:
“Bright
55 Lux to 100 Lux”
55 to 100 Lux
webSocket.SendData() = R0
webSocket.SendData() = R1
webSocket.SendData() = R2
webSocket.SendData() = R3

## Slide 4
B
Yes
Motion sensed?
Light Intensity checked?
No
<35 Lux
> 35 Lux
Light On depends on light intensity
Light Off
Light Off
Display Status on Browser:
“Motion detected, light will on.”
Display Status on Browser:
“Motion detected, brightness more than 35 Lux.”
Display Status on Browser:
“No motion detected in your room.”
Display Status Light on Browser:
“On”
Display Status Light on Browser:
“Off”
Display Status Light on Browser:
“Off”
No
webSocket.SendData() = P0
webSocket.SendData() = P1
webSocket.SendData() = P2

## Slide 5
C
Yes
Button “On” clicked?
No
Light On depends on light intensity
Light Off
Display Status Light on Browser:
“On”
Display Status Light on Browser:
“Off”
Button “Off” clicked?
Yes
No
webSocket.getData() = L1
webSocket.getData() = L0

## Slide 6
D
Humidity and Temperature checked?
<18 °C
18 to 25 °C
>25 °C
Display Status on Browser:
“Too Cold, please on your heater.”
Display Status on Browser:
“Normal Room Temperature”
Display Status on Browser:
“Too Hot, please off your heater.”
No
OLED Display:
Temperature Value and Humidity Value
webSocket.SendData() = T0
webSocket.SendData() = T1
webSocket.SendData() = T2

## Slide 7
E
Yes
Temperature adjust on slider?
No
Temperature adjusted
Display adjusted Temperature Value on Browser
webSocket.getData() = S0 + slider value